## Slide 1
Marcello Ferraro
Advisor: Prof. Carlo Cavallotti
Co-advisor: Dott. Andrea Della Libera
Master degree in Chemical engineering
Milano, 5th October 2023
Fostering Automation in Chemical Kinetics:
Bond Energy Computation and Implementation of a Hierarchical Approach for Thermochemistry

## Slide 2
Outline
Introduction – state of the art in chemical kinetics
Aim of the work
Software development:
  CHEMTP – thermochemical parameters
  InChI2data – automatic input files
  FragsGen – bond energies
Results
Conclusions

## Slide 3
State of art in chemical kinetics
Chemical kinetics knowledge is fundamental for reactor design and CFD studies
Postdictive kinetics
Predictive kinetics
1900
time
2023
2018
Predictive kinetics is based on Potential Energy Surface (PES) exploration and Transition State Theory (TST) rate constants estimation
Powerful chemical kinetics software like EStokTP and Reaction Mechanism Generator (RMG) automatize this calculations

## Slide 4
How to determine rate and thermodynamic parameters accurately and efficiently?

## Slide 5
Thermochemical parameters
Thermochemical parameters are necessary to describe the evolution of energy distribution in reacting environments
Two main possibilities for thermochemical parameters estimation:
Group contribution methods
(Benson - THERM, RMG)
Molecular partition functions +
atomization schemes
(CHEMTP, based on EStokTP)

## Slide 6
Aim of the work
CHEMTP: algorithm for thermochemical parameters estimation
InChI2data: protocol for automatic generation of EStokTP input files
FragsGen: automatic method for bond energies estimation

## Slide 7
Aim of the work
CHEMTP
InChI2data
FragsGen
Thermochemical parameters estimation
Generation of EStokTP input files
Bond enegies estimation
Generation of new software:

## Slide 8
CHEMTP: Connectivity Hierarchy Estimation Model for Thermochemical Parameters
and are calculated exploiting molecular partition functions
is calculated using atomization schemes
Atomization schemes preserve atomic or bond vicinity to construct convenient reactions to calculate ∆H0(0 K) (Connectivity Based Hierarchy approach)
expressed as:
CBH-0
CBH-1
CBH-2
Accuracy

## Slide 9
CBH-0: Isogyric scheme on 2-hydroperoxybutyl
The Isogyric scheme represent every non-hydrogen atom with its corresponding saturated form
CBH-0
CBH-1
CBH-2

## Slide 10
CBH-0: Isogyric scheme on 2-hydroperoxybutyl
The Isogyric scheme represent every non-hydrogen atom with its corresponding saturated form
CBH-0
Methyl
[CH3]
Water
O
Methane
C
[CH2]C(CC)OO + 5 [H][H] → 3 C + [CH3] + 2 O
CBH-1
CBH-2
C4H9O2 + 5 H2 → 3 CH4 + CH3● + 2 H2O

## Slide 11
CBH-1: Isodesmic scheme on 2-hydroperoxybutyl
The Isodesmic scheme preserves every bond environment formed by non-hydrogen atoms
CBH-0
CBH-1
CBH-2
CBH-0 PRODUCTS

## Slide 12
CBH-1: Isodesmic scheme on 2-hydroperoxybutyl
The Isodesmic scheme preserves every bond environment formed by non-hydrogen atoms
CBH-0
Ethyl
[CH3]C
Ethane
CC
CBH-1
CBH-2
Water peroxide
OO
CBH-0 PRODUCTS
[CH2]C(CC)OO + 3 C + O → 2 CC + [CH2]C + CO + OO
C4H9O2 + 3 CH4 + H2O → 2 + + +

## Slide 13
CBH-2: Homodesmotic scheme on 2-hydroperoxybutyl
The Homodesmotic scheme preserves every atom vicinity in terms of type of non-hydrogen atoms and type of bonds
CBH-0
CBH-1
CBH-2
CBH-1 PRODUCTS

## Slide 14
CBH-2: Homodesmotic scheme on 2-hydroperoxybutyl
The Homodesmotic scheme preserves every atom vicinity in terms of type of non-hydrogen atoms and type of bonds
CBH-0
Propane
CCC
[CH2]C(CC)OO + CC + CO → CCC + COO + [CH2]C(C)O
CBH-1
CBH-2
CBH-1 PRODUCTS

## Slide 15
CBH-2: Homodesmotic scheme on 2-hydroperoxybutyl
The Homodesmotic scheme preserves every atom vicinity in terms of type of non-hydrogen atoms and type of bonds
CBH-0
[CH2]C(CC)OO + CC + CO → CCC + COO + [CH2]C(C)O
CBH-1
CBH-2
Methyl peroxide
COO
CBH-1 PRODUCTS

## Slide 16
CBH-2: Homodesmotic scheme on 2-hydroperoxybutyl
The Homodesmotic scheme preserves every atom vicinity in terms of type of non-hydrogen atoms and type of bonds
CBH-0
Propane
CCC
CBH-1
CBH-2
CBH-1 PRODUCTS
Methyl peroxide
COO
[CH2]C(CC)OO + CC + CO → CCC + COO + [CH2]C(C)O
C4H9O2 + + → + +

## Slide 17
Reference species database
[CH2]C(CC)OO + CC + CO → CCC + COO + [CH2]C(C)O
→ EStokTP
) → UNKNOWN
CHEMTP database
→ EStokTP
) → ANL-ATcT1
The database contains 102 reference species ) and at four levels of theory Every reference species pre-selected and optimized
[1]: Argonne National Laboratory – Active Thermochemical Tables
InChI2data used for the automatic generation of EStokTP input files
of

## Slide 18
InChI2data flowchart

## Slide 19
InChI2data flowchart
InChI=1S/C2H6/c1-2/h1-2H3
c1
c2 c1 cc2
h3 c1 hc3 c2 hcc3
h4 c1 hc4 c2 hcc4 h3 dih4
h5 c1 hc5 c2 hcc5 h3 dih5
h6 c2 hc6 c1 hcc6 h3 dih6
h7 c2 hc7 c1 hcc7 h6 dih7
h8 c2 hc8 c1 hcc8 h6 dih8

## Slide 20
InChI2data flowchart
Ready for EStokTP simulation!

## Slide 21
CHEMTP flowchart

## Slide 22
CHEMTP flowchart
[CH2]C(CC)OO + 5 [H][H] → 3 C + [CH3] + 2 O
[CH2]C(CC)OO + 3 C + O → 2 CC + [CH2]C + CO + OO
[CH2]C(CC)OO + CC + CO → CCC + COO + [CH2]C(C)O
Klippenstein et al.2: 4.47 [kcal mol-1]
CHEMTP, CBH-0: -14.69 [kcal mol-1]
CHEMTP, CBH-1: 18.87 [kcal mol-1]
CHEMTP, CBH-2: 4.66 [kcal mol-1]
[2]: Klippenstein, S.J. et al., Journ Phys Chem A, 127-6 1512-1532

## Slide 23
CHEMTP flowchart
Vibrational partition function can not be computed @ 0 K
Thermal correction to 298.15 K based on thermal corrections of single atoms

## Slide 24
CHEMTP flowchart
Fitting on a two set of 7 parameters each over a defined range of temperatures
, , and
C5H8 G 250.000 3000.000 1630.000 1
1.16177281e+01 2.62596289e-02-1.15691725e-05 2.48806136e-09-2.11953159e-13 2
3.62321811e+03-3.45415119e+01-1.80030161e+00 6.93315758e-02-6.40556982e-05 3
3.08708072e-08-5.91217060e-12 7.07276738e+03 3.33132138e+01-1.22550360e+05 4
NASA polynomials
CHEMKIN format

## Slide 25
CHEMTP results: ∆H0(0 K) with ωB97X-D/jun-cc-pVTZ level of theory
Chart: Molecular weight [amu]
| 30.046950191999901 | 44.062600255999897 | 58.078250319999903 | 58.078250319999903 | 72.093900383999994 | 72.093900383999994 | 72.093900383999994 | 86.109550447999993 | 86.109550447999993 | 86.109550447999993 | 100.125200511999 | 100.125200511999 | 100.125200511999 | 114.140850575999 | 114.140850575999 | 128.15650063999999
Alkane | 4.9724 | 3.2141 | 6.2845 | 0.86834 | 9.3439 | 0.1723 | 0.86827 | 0.1797 | 0.81045 | 0.84421 | 0.31158 | 0.83891 | 0.86827 | 0.54855 | 1.2239 | 2.2668
Alkylhydroperoxide | 0.69997 | 0.5885 | 0.023288 | 0.48584 | 0.28136 | 0.57108 | 0.25016 | 0.49731 | 0.092205 | 0.41172 | 0.12032 | 0.4907 | 0.64687 | 0.11765 | 0.30425 | 0.23373 | 0.44217 | 0.22182 | 0.92657 | 1.2442 | 0.14612 | 0.55103 | 0 | 0.17309 | 0.21899 | 1.4271 | 0.32547
Alkylperoxy | 12.4013 | 1.3326 | 5.6444 | 3.5375 | 0.69395 | 1.903 | 1.7971 | 1.4377 | 2.6691 | 0.17383 | 0.086619 | 1.1352 | 1.5378 | 0.2925 | 2.5243 | 0.62455 | 0.25005 | 0.72837 | 2.9339 | 0.39539 | 0.42854 | 24.9543 | 0.20143 | 0.52631 | 23.7114 | 1.3536 | 0.62034
CHEMTP was tested on 142 species by Klippenstein et al.2 database
Average absolute error:
0.39 ± 0.54 [kcal mol-1]
Average relative percentage error:
3.39 ± 5.09
Error caused by:
Different levels of theory used
Different number of sampling points
[2]: Klippenstein, S.J. et al., J. Phys Chem A, 127-6, 1512-1532

## Slide 26
CHEMTP results: ∆H0(0 K) at different levels of theory
Chart: N
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
ωB97X-D | 1.4479 | 0.35083 | 0.58546 | 0.58239 | 0.46494 | 0.23377 | 0.33648 | 0.054197
B2PLYP-D3 | 0.39842 | 0.1443 | -0.32975 | -0.36879 | -0.16998 | -0.10183 | 0.28481 | -0.15082
ωB97X-D-HL | -0.44273 | -0.30129 | 0.25086 | 0.12906 | 0.19266 | -0.050594 | 0.21139 | -0.1991
B2PLYP-D3-HL | -0.080432 | -0.30412 | 0.18479 | 0.070447 | 0.16411 | -0.045568 | 0.20866 | -0.20844
A subset of 8 molecules was used to study the influence of the level of theory on the estimations
ωB97X-D-HL and B2PLYP-D3-HL are CCSD(T) with core electrons correlations and extrapolation to basis set limit, based on ωB97X-D and B2PLYP-D3 results

## Slide 27
CHEMTP results: , , , of isoprene
Chart: Cp0(𝑇) [cal mol-1 K-1]
Chart: S0(𝑇) [cal mol-1 K-1]
Chart: T [K]
Chart: T [K]
[3]: Green, W.H. et al., Comp Phys Comm, 203, 212-225
Isoprene thermochemical parameters from CHEMTP compared with RMG estimations (Benson group contribution method)
Full RRHO was more in agreement with respect to explicit hindered rotor treatment (RRHO-1DHR)
Discrepancy caused by:
Group contribution method different approach
Failure of RRHO at high temperature

## Slide 28
CHEMTP results: , , , of isoprene
Chart: T [K]
Chart: T [K]
Chart: T [K]
Chart: T [K]
[3]: Green, W.H. et al., Comp Phys Comm, 203, 212-225
Isoprene thermochemical parameters from CHEMTP compared with RMG estimations (Benson group contribution method)
Full RRHO was more in agreement with respect to explicit hindered rotor treatment (RRHO-1DHR)
Discrepancy caused by:
Group contribution method different approach
Failure of RRHO at high temperature

## Slide 29
FragsGen flowchart: automatic fragments generation

## Slide 30
FragsGen flowchart: automatic fragments generation
Generation of the Cartesian coordinates of every fragment

## Slide 31
FragsGen flowchart: automatic fragments generation
Conversion to Z-matrix and simulation in EStokTP

## Slide 32
FragsGen results: 1,3-butadiene-2-ol
N | FragsGen[kcal mol-1] | Literature [kcal mol-1]
1 | 144.77 | 174.1[4]
2 | 154.91 | 174.1[4]
3 | 109.86 | 110.7[4]
4 | 85.40 | 84.50[5]
5 | 113.94 | 110.7[4]
6 | 111.32 | 110.7[4]
7 | 107.84 | 90.1[4]
8 | 113.98 | 111.5[6]
[4]: Blanksby S.J et al., Accounts of Chem Research, 36 (4), 255-263
[5]: So S. et al., ACS Earth and Space Chem, 2 (8), 753-763
[6]: Hadad C. M. et al., J. Org. Chem., 63, 8668-8681

## Slide 33
Conclusions
Two challenging tasks in the automation of predictive chemical kinetics are the accurate estimation of thermochemical paramaters and the automatic exploration of PES
EStokTP is a powerful software born and continously updated with this final purpose.
In the present work three codes, working in synergy with EStokTP, were developed:
InChI2data
Automatic generation of EStokTP input files, starting from InChIs identifiers
CHEMTP
Estimation of thermochemical parameters based on partition functions + atomization schemes
FragsGen
Automatic generation of fragmentation products and estimation of bond energies

## Slide 34
Thanks for the kind attention!
Any questions?